## Slide 1: DEKA Protius/Daisy IFU
4.19.21 – Draft 1

## Slide 2: IFU
Cleanse hands (hand washing with soap & water and/or hand sanitizer)
Choose delivery site & clean 2-inch area with a sterile alcohol prep pad
  Recommend non-dominant forearm (palm side) or either mid-to-upper outer thigh
  Do not use arm on the side of a prior mastectomy, if possible
  Do not use paralyzed limb, if possible
  Delivery site should be free of pain, lumps, swelling, warmth, wounds, bruising, redness, infections, implanted ports or other devices
  May be given through a tattoo
Remove applicator patch from packaging
Hold top of device in dominant hand and peel off removable liner from the flat side of the applicator with non-dominant hand

## Slide 3
Grasp the device firmly from the top and place the applicator securely onto skin at the pre-selected cleansed delivery site
Push the center of the applicator firmly into skin to invert device “petals” and deliver vaccine
  Expect skin to be spread taut beneath the applicator)
Leave the applicator in place for XX seconds
To remove, quickly peel the applicator from skin
  Hold pressure to site as necessary
Cleanse hands
Return applicator to pharmacist for disposal and complete required observation period. Report adverse reactions.